## Slide 1: Using the lattice Boltzmann method to model tidal flows within Dover Harbour.
By Andrew Cunningham, Jian Zhou and Jon Shiach
Centre for mathematical modelling and flow analysis, Department of Computing and Mathematics, Manchester Metropolitan University, Manchester, M1 5GD

## Slide 2: Presentation Outline
Introduction
Methodology
Validation
Results
Conclusion

## Slide 3: Introduction

## Slide 4: Introduction
What are we studying?
  The effect of tidal flows within Dover Harbour.
Why are we studying this?
  Dover Harbour requires dredging of up to 250,000m3 of sand and mud per annum.
How we are going to study it?
  The harbour will be observed and mapped using the lattice Boltzmann method based on both tidal flow patterns and topological data.
Aerial view of Dover Harbour
Notes: What are we studying?
I have been studying the effects of turbulent flows surrounding renewable devices. To meet current legislation by 2020 the UK must have a reliance of around 15% upon renewable sources, including heat, transport and electricity (Coskeran, 2010, National Renewable Energy Plan for the UK). Many other EU countries have achieved this standard and yet the UK is flagging behind. The UK is in a more favourable position for being an island and the tidal potential of around 500 – 1000 TWh/year threshold (Burrows, 2015). Unfortunately, due to funding, the tidal barrage plan for Swansea did not proceed and therefore we have swapped to another device as there have been reports that the Whirlpool turbine device could be implemented into more remote areas of the UK with access to a river.

## Slide 5: Revival of the Western Harbour

## Slide 6: Revival of the Western Harbour
Dover Harbour 2015
Dover Harbour 2019

## Slide 7: Methodology

## Slide 8: Lattice Boltzmann method (LBM)
For these simulations the single-relaxation time method was used.
Where f and feq are the distribution function and the equillibirum distribution function respectively, ei is the discrete velocity vector and the relaxation time.
The macroscopic variables for density () and velocity () are found through
Fig 1 A D2Q9 lattice configuration
1
2
3
4
5
6
7
8
0

## Slide 9: Particle Distribution

## Slide 10: Lid-Driven cavity problem
Fig 5 Lid Driven Cavity (Perumal and Dass, 2013)
Upstream Secondary Vortex
Primary Vortex
U = 0
V = 0
U = 0
V = 0
Upstream Secondary Bottom Vortex
Downstream Secondary Bottom Vortex
U = 0, V = 0
U = u, V = 0

## Slide 11: Idealised Harbour Design
Inflow
Outflow

## Slide 12: Boundary conditions (Bounceback / Non-slip)

## Slide 13: Boundary Conditions (Zou – He)
Dotted lines depict a Zou-He boundary condition.
  = f9 + f1 + f3 + 2*( f2 + f6 + f5 )
  f4 = f2 – (2/3)* *uy
  f8 = f6 + (1/2)*(f4 – f2) + (1/2)* *ux – (1/6)* *uy
  f7 = f5 + (1/2)*(f4 – f2) - (1/2)* *ux – (1/6)* *uy

## Slide 14: Validation

## Slide 15: Benchmark of the lid-driven cavity using (Ghia1982)
Chart: Vertical velocity of lid-driven cavity
Analytical 100 | 0 | 0.09233 | 0.10091 | 0.1089 | 0.12317 | 0.16077 | 0.17507 | 0.17527 | 0.028805 | -0.24533 | -0.24533 | -0.17858 | -0.12037 | -0.10781 | -0.094406 | 0
Analytical 1000 | 0 | 0.27485 | 0.29012 | 0.30353 | 0.32627 | 0.37095 | 0.36936 | 0.36392 | 0.02526 | -0.35764 | -0.49242 | -0.53953 | -0.032659 | -0.027566 | -0.022522 | 0
Analytical 3200 | 0 | 0.3956 | 0.40917 | 0.41906 | 0.42768 | 0.37119 | 0.35013 | 0.33991 | 0.00999 | -0.31544 | -0.42953 | -0.55816 | -0.34077 | -0.28764 | -0.23303 | 0
Analytical 5000 | 0 | 0.42447 | 0.43329 | 0.43648 | 0.42951 | 0.35368 | 0.30455 | 0.29303 | 0.00945 | -0.28176 | -0.36857 | -0.51418 | -0.43116 | -0.37029 | -0.30314 | 0
Chart: Horizontal velocity lid-driven cavity
Analytical Re100 | 0 | 0.0547 | 0.0625 | 0.0703 | 0.1016 | 0.1719 | 0.2813 | 0.4531 | 0.5 | 0.6172 | 0.7344 | 0.8516 | 0.9531 | 0.9609 | 0.9688 | 0.9766 | 1
Analytical 1000 | 0 | 0.0547 | 0.0625 | 0.0703 | 0.1016 | 0.1719 | 0.2813 | 0.4531 | 0.5 | 0.6172 | 0.7344 | 0.8516 | 0.9531 | 0.9609 | 0.9688 | 0.9766 | 1
Analytical 3200 | 0 | 0.0547 | 0.0625 | 0.0703 | 0.1016 | 0.1719 | 0.2813 | 0.4531 | 0.5 | 0.6172 | 0.7344 | 0.8516 | 0.9531 | 0.9609 | 0.9688 | 0.9766 | 1
Analytical 5000 | 0 | 0.0547 | 0.0625 | 0.0703 | 0.1016 | 0.1719 | 0.2813 | 0.4531 | 0.5 | 0.6172 | 0.7344 | 0.8516 | 0.9531 | 0.9609 | 0.9688 | 0.9766 | 1
Fig 6 Vertical velocity compared with Ghia’s results
Fig 7 Horizontal velocity compared with Ghia’s results

## Slide 16: Results

## Slide 17: Before the Revival
Dover Harbour 2015
Dover Harbour 2019

## Slide 18: Dover Harbour Topology
Shallow
Deep
<0m
>50m

## Slide 19: SWE Tidal Mean Flow

## Slide 20: Tidal plot
Chart: Mean tidal depth for week starting 27/01/2020
Actual data | 6.33 | 1.14 | 6.45 | 1.29 | 6.25 | 1.18 | 6.38 | 1.34 | 6.14 | 1.26 | 6.14 | 1.45 | 6.27 | 1.4 | 6 | 1.61 | 6.13 | 1.59 | 5.84 | 1.82
LBM SWE data | 5.996 | 2.004 | 6.1751 | 2.1107 | 5.6061 | 1.8267 | 5.8563 | 1.8163 | 5.9835 | 1.9906 | 5.9835 | 2.087 | 5.9762 | 2.0162 | 5.8908 | 1.9306 | 5.9516 | 1.9115 | 5.9721 | 1.9628

## Slide 21: Dredging or deepening of the Outer Harbour Area
Current Harbour Depth
Increased Depth of 20m

## Slide 22: Conclusions

## Slide 23: Conclusions
The new expansion does not seem to have a major impact upon the flow within the harbour.
The entrances to the harbour are the main areas of concern with them being the areas of high turbulence which would increase the amount of sediment drop off.
Further work with sediment transport can be conducted to further examine the entrances to the harbour.
The SWE can predict the tidal patterns within the harbour to an appropriate degree.
Increasing the depth through dredging looks to be a good short term answer to the build up of silt along the harbour floor.

## Slide 24: Advection Diffusion
Non-linear would not work with SWE.

## Slide 25: References
Ghia, U, K N Ghia, and C T Shin (1982). High-Resolutions for Incompressible Flow Using the Navier-Stokes Equations and a Multigrid Method. Tech. rep., pp. 387–411.
Perumal, D. Arumuga and Anoop K. Dass (2013). “Application of lattice Boltzmann method for incompressible viscous flows”. In: Applied Mathematical Modelling 37.6, pp. 4075–4092
Wolfram, Stephen (1994). Cellular Automata and Complexity: Collected Papers.
Zou, Qisu and Xiaoyi He (1997). “On pressure and velocity flow boundary conditions and bounce-back for the lattice Boltzmann BGK model”. In: Physics of Fluids 9.6, pp. 1591–1598.

## Slide 26: Thank You Any Questions?